Take a picture of setup

procedure

Week 1 Instructions: Exploring the Onset of Chaos

Objective
To study the onset of chaos in a nonlinear RLC circuit and begin observing period doubling, chaotic behavior, and bifurcation patterns.

Week 1 Tasks

Task A: Nonlinear RLC Circuit

1.Setup:
   - Assemble the nonlinear RLC circuit as shown in the diagram.
   - Use a sine wave generator set at ~12 kHz and 10 V amplitude. Connect an oscilloscope to monitor \( V_R \) and \( V_0 \).

2. Initial Observations:
   - Use the oscilloscope in time mode and Lissajous mode to view \( V_R \) and \( V_0 \).
   - Adjust the frequency near resonance without distorting the sinusoidal waveform.

3. FFT Analysis:
   - Analyze the spectrum with an FFT (frequency span set to 12.5 kHz).
   - Observe peaks, including any frequency doubling, by adjusting the driving frequency.

4. Observing Period Doubling:
   - Gradually increase \( V_0 \) while observing changes in Lissajous figures and FFT peaks.
   - Look for evidence of period doubling and chaotic transitions.

5. Data Collection:
   - Record waveform data showing at least two period doublings (e.g., 4 peaks in FFT or a 4-loop Lissajous figure).
   - Save waveform and Fourier spectrum data for analysis in MATLAB.

6. Bifurcation Diagram:
   - Plot \( V_R \) against \( V_0 \) for different values, capturing periodicity changes at doubling points.
   - Identify threshold values where period doubling occurs.

7. Feigenbaum Constant:
   - Use data to calculate the Feigenbaum constant \( \delta \) and estimate \( a_\infty \), validating results with theoretical values.

Deliverables
- Plots of \( V_R \) vs. time, Lissajous curves, and FFT spectra for each phase.
- A bifurcation diagram detailing period doubling points.
- Calculations and estimates for \( \delta \) and \( a_\infty \).

Complete all data acquisition and preliminary analysis before Week 2.